|  | Model | NBD8904R-PL |
| --- | --- | --- |
| System | Main processor | Hi3536D |
|  | Operating System | Embedded Linux |
|  | System resources | Simultaneous multi-channel real-time recording, playback, network operation, USB backup |
| Interface | Operator interface | 16-bit true color graphic menu operation interface, support mouse operation |
|  | Preview | 1/4 |
| Video | Video input (IP) | 4*1080P |
|  | Access bandwidth | 24Mbps |
|  | Forwarding bandwidth bandwidth | 24Mbps |
|  | Video compression | H.265/H.264 |
|  | Display quality | Max:1920*1080 |
|  | Playback quality | 1080P |
|  | Decode | 1*1080P |
|  | VR | Unsupport |
|  | Motion detection | Support(depend on camera) |
| Audio | Audio compression | G.711A |
|  | Intercom | Unsupport |
| Record & playback | Recording mode | Manual>Alarm>Dynamic Detection>Timing |
|  | Local payback | 1*1080P |
|  | Search mode | Search by Time/Calendar/Event/Channel |
|  | Record storage | HDD、Network |
|  | Backup mode | Network backup, USB hard disk, USB burner, SATA burner |
| External interface | Video output | 1ch VGA，1ch HDMI HD output |
|  | Audio I/O | 0/1 |
|  | Alarm I/O | 0/0 |
|  | Network interface | 1*RJ45 10M/100M Adaptive Ethernet port，4* POE ports |
|  | USB interface | 2*USB2.0 ports |
|  | HDD | 1*SATA(Up to 8TB for each disk) |
|  | ESATA | No |
|  | Serial interface | No |
| Other | ONVIF | Support |
|  | Power supply | Input：DC48V,PoE Output：15.4W |
|  | Power Consumption | <10W(Without HDD) |
|  | Work environment | Temperature:0℃-＋55℃ , Humidity:10%－90%RH , Atm:86kpa－106kp |
|  | Dimension | 137.5mm*82mm+88mm*79.4mm |
|  | Weight | A total of about 156g |

# Text boxes

NBD8904R-PL

4ch 1080P POE H.265 NVR Board

Feature：

- Support HDMI VGA HD output;

- Support ONVIF;access third party;

- Support web, CMS, center platform management software MYEYE, provide SDK development;

- Support multiple cloud technology, network penetration, alarm information pushed to your phone and other functions;

- Support multiple network services (support DHCP, FTP, DNS, DDNS, NTP, UPNP, EMAIL, IP searches, Alarm Center, etc.);

12V OUTPUT

MDIO BUS

12V INPUT

79.4mm

1*SATA

137.5mm

88mm

82mm

RJ45

4*POE

48V Input

MDIO BUS

HDMI

NET

2*USB2.0

Audio output

VGA

USB

Parameters：

Model：NBD8904R-PL